Furnace User Manual
Basic information
Name of property	JH-6 Furnace
Property No.	3100403035-850
Size	Internal dimensions W40*D40*H40(cm) / External dimensions W68*D69*H100(cm)
Temperature range	1200℃
Voltage	220V /50A
Purchase date	1090907

Instructions
1. Turn on the power。
2. Put samples into the furnace，close thedoor.
3. Use ▲ and ▼ to set the temperature.
4. Then click ENT to finish setting。
5. OUT1 light on，it is mean the equipment is heating.
6. When the temperature reaches the setting poing, the light will blink.
7. Turn off the power after use。
8. When taking the samples in and out, must wear insulation gloves
9. Scan the qr-code to fill the google form to submit the usage or through the link: https://forms.gle/kw8VCQvomJWE3cUP6